Figure of Merit for Reversible Logic Systems

Technical report ZF011 v1, June 6, 2022

Erik P. DeBenedictis
Zettaflops, LLC, Albuquerque, NM 87112
erikdebenedictis@zettaflops.org

# Abstract

This document proposes a figure of merit RFOM for transistor-based reversible logic. The belief is that reversible logic is ready for investment as a near-term opportunity, although there are also longer-term opportunities. As an example of the use of the figure of merit, investors expect a 10× improvement over the state of the art (CMOS) before funding product development, with this document providing a basis for such determinations.

This document proposes RFOM, which is the overall wall-plug energy efficiency improvement factor for a reversible transistor circuit compared to CMOS. This would be a number > 1, e. g. RFOM of 10 would indicate 1/10th the energy in comparison to CMOS for an equivalent function.

The original reversible logic concept depended on three factors, the 2RC/ energy factor of the logic, the efficiency of the energy-recycling power supply, and a dissipation floor that depends on static leakage. Recently, a cryo-adiabatic power train has been proposed that also depends on a cooling overhead.

# Introduction and Reference model

The reference model below shows reversible logic from the perspective of energy flow. The system is powered by electricity arriving from above (blue), which is all ultimately turned into heat (red), with the desirable side-effect of producing as much computing (green) as possible.

Reversible logic circuits eject a portion GL of their input energy in a form that may be suitable for recycling. In the original formulation of reversible logic from the 1990s, recyclable energy was sent to an energy recycling power supply, which would send a portion GP of the recyclable energy back to the chip. As will be explained below, the system-level energy efficiency rises toward a singularity as the product GLGP approaches 1.

The reversible chip can run in a cryocooler, removing heat with an energy overhead factor, called specific power, PS. Specific power is in units of Watts per Watt and is the amount of power that must be added per unit of power removed from the cryostat.

This document applies to both cryogenic and room temperature operation. If the reversible chip is in a cryostat, the energy overhead factor PS should correspond to the cryocooler in use, otherwise use PS = 0. Likewise, use GP = 0 if there is no energy recycling. The figure of merit will accurately represent a system with both a cryocooler and an energy recycling power supply.

The objective of this document is to provide a figure of merit for a reversible logic system that includes the factors PS, GL, GP, and the leakage parameters Ioff/Ion. This will allow consistent comparison of proposed transistorized reversible logic systems, specifically addressing situations where some parameters are left out or they are combined improperly.

# Model

Say the power-clock supply sends energy E1 to a reversible chip. The chip dissipates fraction 2RC/, returning fraction GL = 1 ( 2RC/ to the power supply.

Thus, GL is defined as the fraction of the power-clock energy that the reversible logic chip does not turn into heat, instead returning it to the power supply. GL is a sub unity gain factor.

GP is defined as the fraction of the power-clock energy returned to the power supply that can be successfully recycled, leading to an additional fraction GLGP being sent to the reversible chip.

Thus, GP is defined as the energy recycling efficiency of the power supply. GP is also a sub unity gain factor.

This process will repeat, so the chip receives not only E1, but additional energy that has been recycled one or more times, eventually receiving

S = E1 ( 1 + GLGP  + GL2GP 2 + …),

which is a series that sums to

S = E1 / (1 ( GLGP) = ½CV2.

Thus, S is the “portion” of the original energy E1 that arrives at the chip, although notably a portion > 1. Since we have not said how much energy was sent in the first place, the equation above defines E1 based on the reversible chip having received ½CV2, or the energy necessary to charge a signal node.

# Comparison to CMOS

Let us now compute the RFOM as the energy of a CMOS circuit divided by the energy of a reversible circuit. We will assume the same transistors are in both circuits. We will also assume that there are the same number of transistors and that average R and C parameters will be the same between CMOS and reversible circuits. The latter assumptions will be approximately correct, yet there is room for debate.

This section will compute RFOM starting with EC/ER. EC/ER is the CMOS (C) total energy divided by the reversible (R) total energy.

From above, E1 is

E1 = S (1 ( GLGP),

so let us define E2 to be energy consumed by the cryocooler,

E2 = S (1 ( GL)PS,

where PS is the wall-plug energy required to remove one unit of heat. PS will depend on the temperature, but this document will never need to reference the temperature directly. As stated previously, use PS = 0 for a room-temperature computing system.

The total energy drawn from the wall plug to charge a reversible signal node is,

ER = E1 + E2 = S ((1 ( GLGP) + (1 – GL)PS).

Let us define E3 to be energy dissipated by CMOS,

E3 = S,

and E4 for the cryocooler,

E4 = S PS,

for a total EC of

EC = S (1 + PS).

Hence,

ER/EC = S ((1 ( GLGP) + (1 – GL) PS) / S (1 + PS)

= ((1 ( GLGP) + (1 – GL) PS) / (1 + PS),

which after some algebraic rearrangement yields

ER/EC = 1 – GL(GP + PS)/(1 + PS)

The readers attention is called to the term (GP + PS)/(1 + PS). If PS = 0, the term is equal to GP, but if PS = (, the term is equal to 1. So, PS is a “control knob” that causes to GP to disappear.

# RFOM and summary

Repeating the definitions:

PS is the specific power, or cooling overhead, of the cryocooler, with PS = 0 if there is no cryocooler.

GL is the portion of the power-clock energy that the reversible chip does not turn into heat, but returns to the power supply.

GP is the energy recycling efficiency of the power supply.

Ioff and Ion are the on and off current of a typical transistor.

We will now compute RFOM, yet the most concise formulation computes the max of the lowest energies and then inverts the result, which is

- If PS = 0, indicating room temperature operation, ER/EC = 1 ( GLGP, showing that the energy efficiency improvement of the reversible circuit is in series with the energy recycling of the power supply. It is possible to trade off GL for GP, but neither factor can exceed 1. This highlights the importance of considering both the energy efficiency of a reversible chip and energy recycling power supply together.

- If PS = (, the limit of cryo operation, ER/EC = 1 ( GL, showing that a cryocooler can substitute for the energy recycling power supply. A cryocooled reversible implementation may be more energy efficient than a cryo CMOS implementation, but both are likely to be less efficient than a pure room temperature implementation. Thus, cryo operation is most likely to be valuable when there is an external problem constraint requiring computing at a specific temperature, such as quantum computing.

- If GP = 0, indicating no energy recycling power supply, ER/EC = 1 ( GLPS /(1 + PS), which suggests that GL ( PS/(1 + PS). In other words, a 1,000× energy efficiency improvement may be possible for 4 K operation where the cooling overhead is typically PS = 1,000 W/W, but such a boost would not be possible at 77 K because PS will be too small. So, a large GL can be spoiled by a small PS.

# Text boxes

Leakage not illustrated

Computing

Electricity

Heat

Cooler
PS ( 0

Energy recycling
 power supply
GP < 1

Reversible chip
GL < 1

1 + PS

GP + PS

RFOM = max(1 – GL              ,         )-1

Ion

Ioff